## Slide 1: CS 31007 Autumn 2020 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty
Bhargab B. Bhattacharya
Week 6: October 05, 2020
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 2: So far covered in computer arithmetic…
Number Systems and Overflow
Ripple-Carry Adder (RCA)
Carry-Lookahead Adder (CLA)
Hybrid Adder, CLT
Carry-Select Adder (CSA)
Brent-Kung’s Parallel Prefix Adder (PPA)
Carry-Save Adders (for adding multiple operands)
Today: Integer Multiplication
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 3: Integer Multiplication

## Slide 4: Multiplication
  Multiplicand
  Multiplier
  Partial products
  Final sum
Base 10: 8 × 5 = 40
  => 32 + 0 + 8 = 40
How wide is the result?
  => log(n × m) = log n + log m
  => 32-bit × 32-bit = 64-bit result
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | × | 0 | 1 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 1 | 0 | 0 | 0 |  | 
 | 0 | 0 | 0 | 0 |  |  | 
 | 0 | 1 | 0 | 1 | 0 | 0 | 0
+ 8
+ 5
- 8
+5
unsigned
2’s compl.
Can you notice the need for Carry-Save Addition? We need to add multiple numbers!

## Slide 5: CARRY-SAVE ADDER (addition of multiple operands)
Add four 4-bit integers, A, B, E, F

## Slide 6: Unsigned Multiplication
Ai and Bi are all 0 or 1

## Slide 7: Multiplication
More complicated than addition
  Accomplished via
  Array multipliers
  shifting and repeated addition
More time and more area 0101 0010 (multiplicand) x 0110 1101 (multiplier)
Negative numbers: convert and multiply
Use other better techniques like Booth’s encoding

## Slide 9: Array Multiplier Using Carry-Save Adders
Carry-Save Adder

## Slide 10: Array Multiplier Using Carry-Save Adders (CSA
CLT

## Slide 11: 16-bit Array Multiplier
Conceptually straightforward
Fairly expensive hardware, integer multiplies relatively rare
  Mostly used in array address calc: replace with shifts
[Courtesy: J. Hayes, Univ. of Michigan]

## Slide 12: Multiplication (Shift and Repeated Additions)
Mimic the multiplication process in hardware
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication

## Slide 13: Explanations
Multiplicand register is kept 64-bit wide because 32-bit multiplicand will be shifted 32 times to the left
  Requires a 64-bit ALU
Product register must be 64-bit wide to accommodate the result
Contents of multiplier register is shifted 32 times to the right so that each bit successively appears as the least significant bit (LSB) to be checked by the controller

## Slide 14: Multiplication Hardware
Initially 0

## Slide 15: A Little Optimized Version

## Slide 16: Further Optimized Version of Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
Multiplier
(32-bits)

## Slide 17: Optimized Multiplication: Implementation

## Slide 18: Multiplication Example
0010 × 0110 = ? 0010 (+ 2, multiplicand); 0110 (+ 6, multiplier)
+12
logical shift

## Slide 19: Signed Multiplication
Recall
  For p = a × b, if either a < 0 or b < 0, then p < 0
  If (a < 0 and b < 0) or (a > 0 and b > 0) then p > 0
  Hence sign(p) = sign(a)  sign(b)
Hence
  Convert multiplier and multiplicand to positive number each
  Multiply two positive numbers
  Compute sign, convert product accordingly

## Slide 20: Booth’s Encoding (valid for signed multiplication as well)
Recall old trick
  When multiplying by 9:
    Multiply by 10 (easy, just shift digits left)
    Subtract once
  e.g.,
    123454 × 9 = 123454 × (10 – 1) = 1234540 – 123454
    Converts addition of six partial products to one shift and one subtraction
Booth’s algorithm applies the same principle
  in binary we have just ‘1’ and ‘0’

## Slide 21: Booth’s Encoding
Multiply x by 0111
x (multiplicand); 0111 (multiplier) => x ×7
Search for a run of ‘1’ bits in the multiplier
  e.g. ‘0111’ has a run of 3 ‘1’ bits in the middle
  Multiplying by ‘0111’ (7 in decimal) is equivalent to multiplying by 8 and subtracting once, since
  x ×7 = x ×(8 – 1) = 8x – x =>(shift-left x, three times) - x
Hence, iterate right to left and look for “runs of 1”:
  Subtract multiplicand from product at first ‘1’
  Shift multiplicand by 3-bits on left and add to the partial product after the last ‘1’
  Do nothing for the consecutive 1-bits/in the middle, or for 0-runs (actually, we keep on shifting the product register)

## Slide 22: Booth’s Encoding for Multiplier
0 1 0 0 0 0 1 1 1 1 0 0
beginning of 1-run (10)
middle of 1-run (11)
end of 1-run (01)
0-run (00)

## Slide 23: Booth’s Algorithm
Current bit | Bit to right | Explanation | Example (multiplier) | Operation
1 | 0 | Begins run of ‘1’ | 00001111000 | Subtract/shift
1 | 1 | Middle of run of ‘1’ | 00001111000 | Nothing/shift
0 | 1 | End of a run of ‘1’ | 00001111000 | Add/shift
0 | 0 | Middle of a run of ‘0’ | 00001111000 | Nothing/shift

## Slide 24: Booth’s Encoding
Really just a new way to encode numbers
  Normally positionally weighted as 2n
  With Booth, each position has a sign bit
  Can be extended to multiple bits
0 | 1 | 1 | 0 | Binary
+1 | 0 | -1 | 0 | Booth’s encoding

## Slide 25: Booth’s algorithm: Example
0010 × 1101 = ? 0010 (+ 2, multiplicand); 1101 (- 3, multiplier)
-6
op performed in the left half
arithmetic shift
initialization
start of
1-run
end of
1-run

## Slide 26: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd

## Slide 27: CS 31007 Autumn 2020 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty
Bhargab B. Bhattacharya
Week 6: October 06, 2020
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 28: So far covered in computer arithmetic…
Integer Number Systems and Overflow
Ripple-Carry Adder (RCA)
Carry-Lookahead Adder (CLA)
Hybrid Adder, CLT
Carry-Select Adder (CSA)
Brent-Kung’s Parallel Prefix Adder (PPA)
Carry-Save Adders (for adding multiple operands)
Integer Multiplication
Today
Integer Division
Floating-Point Arithmetic and Hardware
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 29: Division
Implemented by successive subtractions
Result must verify the equality
Dividend = (Multiplier × Quotient) + Remainder

## Slide 30: Decimal division
What are the rules?
  Repeatedly try to subtract a multiple of divisor from dividend
  Record multiple (or zero)
  At each step, repeat with a lower power of ten
  Stop when remainder is smaller than divisor
 | 303
7 | 2126
 | -210
 | 26 -21 5

## Slide 31: Integer Division in Binary
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 32: Integer Division
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 33: Division Hardware
Initially dividend
Initially divisor in left half

## Slide 34: Restoring Division

## Slide 35: Optimized Divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both

## Slide 36: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi, mflo to access result

## Slide 37: MIPS Architecture for Integer Arithmetic: Multiplication and Division

## Slide 38: Floating Point: Format, Arithmetic, and Hardware Implementation
instruction set
software
hardware

## Slide 39
The IEEE Floating-Point Standard

## Slide 40: A computation error observed by a UG student led to the ACM Turing Award later ….
1953: Willian Kahan, a UG student of Math at the University of Toronto was simulating numerically the dynamics of the wing controller of an aircraft during take-off and landing
Observed certain unexpected results due to errors in computation
=> concept of floating-point (FP) arithmetic
=> principal architect behind IEEE 754 FP standard (1985)
=> Kahan honored with ACM Turing Award (1989)
William Kahan (1933 - )

## Slide 41: Floating-Point Representation
Used to represent real numbers
Defined by IEEE 754 Standard
--- Kahan (1985)
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)
  Infamous Intel Pentium Bug (1994) =>FDIV => loss of $300 Million

## Slide 42: Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized
§3.5 Floating Point

## Slide 43: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Normalized Significand is Mantissa with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1023
  Trade-off between range (E) and precision (M)
S
Exponent
Mantissa (M)
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
Fraction
Mantissa
 Significand

## Slide 44
IEEE 754 Single-Precision Floating-Point
Representation of floating point numbers in IEEE 754 standard:
single precision
1
8
23
sign
FP-exponent E:
excess 127 binary coding
mantissa:
sign + magnitude, normalized
binary significand w/ hidden
integer bit: 1.M
Actual exponent is e = E – 127
Floating-point exponent E = e + 127
S
E
M
FP-exponent (E) Actual exponent e
00000000 (0) Special use
00000001 (1) - 126
00000010 (2) - 125
…………. …….
01111111 (127) 0
…………. …….
11111110 (254) + 127
11111111 (255) Special use

## Slide 45: IEEE 754 floating-point standard
Leading “1” bit of significand is implicit
Exponent is “biased” to make comparison easier
  all 0s is smallest exponent; all 1s is largest
  bias of 127 for single precision and 1023 for double precision
  summary: (–1)sign ´ (1+significand) ´ 2exponent – bias
Example 1 (Encoding):
For a given decimal number, construct its FP-representation
  decimal: - 0.75
   binary: - 0.11 = - 1.1 x 2-1 (normalized)
   Floating-point exponent = - 1 +127 = 126 = 01111110
  IEEE single precision:
  - 0.75 = 1 01111110 10000000000000000000000

## Slide 46: Decoding a floating-point number
Sign indicated by first bit S  (-1)S
Subtract 127 from biased exponent E to obtain the actual exponent e = E - 127
Number in binary = (-1)S 1.M × 2e
S
E
M

## Slide 47: Example 1
Sign bit is zero: Number is positive
Biased exponent E = 01111111 |2 = 127;
Actual exponent e = E – 127 = 0  20
Mantissa is all-zero  1.0 (restored the hidden bit)
The number = + 1.0  20 |2 =1.0|10
0
0111 1111
0000 0000 0000 0000 0000 000

## Slide 48: Example 2
Sign bit is zero: Number is positive
Biased exponent E = 1000 0000 |2 = 128;
Actual exponent e = E – 127 = 1  21
Significand  1.1 (restored the hidden bit)
The number = + 1.1  21 |2 = + 11 |2 = + 3.0|10
0
1000 0000
1000 0000 0000 0000 0000 000

## Slide 49: Example 3
Sign bit is one: Number is negative
Biased exponent E = 0111 1110 |2 = 126;
Actual exponent e = E – 127 = - 1  2-1
Significand  1.11 (restored the hidden bit)
The number = - 1.11  2-1 |2 = - 0.111 |2 = -0.875|10
1
0111 1110
11000000000000000000000000000

## Slide 50: Example 4
What number is represented by the single-precision float
1 10000001 01000………00
  S = 1
  Mantissa = 01000…002
  FP-Exponent = 100000012 = 129
N = (–1)1 × (1 + .012) × 2(129 – 127)
  = (–1) × 1.01 × 22
  = –101|2 = – 5.0|10

## Slide 51: Example 2 (Encoding)
Represent –2 in FP-format
  Convert to binary: 10
  Normalize: 1.0×21
  Sign bit is 1
  FP-exponent is 127 + 1 = 128 = 10000000two
  Mantissa is 00…0
1
1000 0000
0000 0000 0000 0000 0000 000

## Slide 52
How do I represent zero then ?  1. M × 2E -127
FP-exponent (E) Actual exponent e
00000000 (0) Special use
00000001 (1) - 126
00000010 (2) - 125
…………. …….
01111111 (127) 0
…………. …….
11111110 (254) + 127
11111111 (255) Special use
* Any non-zero number that is smaller than the smallest normalized FP-number is a denormal number (consider magnitude only)
0/1
0000 0000
0000 0000 0000 0000 0000 000

## Slide 53: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Mantissa: 000…00  normalized significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Mantissa: 111…11  normalized significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 54: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Mantissa : 000…00  norm. significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Mantissa: 111…11  norm significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 55: Floating-Point Precision
Relative precision
  all mantissa-bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 56: Single-Precision Normalized Range
Exponents 00000000 and 11111111 reserved
Smallest value
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
  Largest value
  = ±(2.0 – 2-23) × 2+127 ≈ ±3.4 × 10+38
0/1
0000 0001
0000 0000 0000 0000 0000 000
0/1
1111 1110
1111 1111 1111 1111 1111 111
+1.0 × 2–126
-1.0 × 2–126
≈ +2.0 × 2+127
≈ -2.0 × 2+127
0
+ve-overflow
representable normalized +ve FP-numbers
-ve overflow
+ve
under-flow
-ve
under-flow
real line
representable normalized -ve FP-numbers

## Slide 57: Single-Precision FP-Denormal Numbers
Exponents 00000000 and 11111111 reserved
Smallest value (normalized)
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
  Denormal numbers (gradual underflow)
  = ± 0.M × 2-126 {min: ± 2-23 × 2-126; max: ± (1-2-23 ) × 2-126}
0/1
0000 0001
0000 0000 0000 0000 0000 000
0/1
0000 0000
M  0
+1.0 × 2–126
-1.0 × 2–126
≈ +2.0 × 2+127
≈ -2.0 × 2+127
0
overflow
representable normalized +ve FP-numbers
overflow
under-flow
under-flow
real line
representable normalized -ve FP-numbers

## Slide 58: Denormal FP-Numbers
Exponent = 000...0  hidden bit is 0
Smaller than normalized numbers
  allow for gradual underflow, with diminishing precision
Denormal with mantissa = 000...0
 +0, -0
N

## Slide 59: Infinities and NaNs
Exponent = 111...1, Mantissa= 000...0
  ± Infinity
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, Mantissa ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0, -3
  Can be used in subsequent calculations

## Slide 60: Floating Point Complexities
Operations are somewhat more complicated
In addition to overflow, we may have “underflow”
Accuracy can be a big problem
  IEEE 754 keeps three extra bits, guard, round, and sticky
  several rounding modes
  Non-zero number divide-by-zero yields “infinity”  overflow
  Non-zero number divide-by-infinity yields  underflow
  zero divide-by-zero yields “not a number (NaN)”
Implementing the standard can be tricky
Not using the standard can be even worse
Remember the 1994 Pentium FDIV bug; write-off cost US$ 300 M

## Slide 61: Floating-Point Addition
Consider a 4-digit decimal example
  99.99 + 0.1610
1. Align decimal points
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102

## Slide 62: Floating-Point Addition
Alignment
The proper digits have to be added
Addition of significands
Normalisation of the result
Rounding
Example in decimal system
precision 4 digits
What is 9.999 • 101 + 1.610 • 10-1 ?
Result: 1.002 • 102

## Slide 63: FP-Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined

## Slide 64: Floating-Point Addition
0
0111 1111
0000 0000 0000 0000 0000 000
0
1000 000
1000 0000 0000 0000 0000 000

## Slide 65: FP-Adder Hardware
Step 1
Step 2
Step 4
Step 5
compare exponents
equalizing exponents
Integer addition
Step 3
normalize
round
Result

## Slide 66: Floating-Point Multiplication
Consider a 4-digit decimal example
  (1.110 × 1010 ) × (9.200 × 10–5 )
1. Add exponents
  For biased exponents, subtract bias from sum
  New exponent = 10 + –5 = 5
2. Multiply significands
  1.110 × 9.200 = 10.212  10.212 × 105
3. Normalize result & check for over/underflow
  1.0212 × 106 (Increment the exponent if needed)
  4. Round and renormalize if necessary
  1.021 × 106
5. Determine sign of result from signs of operands
  +1.021 × 106

## Slide 67: Floating-Point Multiplication
Now consider a 4-digit binary example
  1.0002 × 2–1 × –1.1102 × 2–2 (0.5 × –0.4375)
1. Add exponents
  Unbiased: –1 + –2 = –3
  Biased: (–1 + 127) + (–2 + 127) = –3 + 254 – 127 = –3 + 127
2. Multiply significands
  1.0002 × 1.1102  1.1102 × 2–3
3. Normalize result & check for over/underflow
  1.1102 × 2–3 (no change) with no over/underflow
4. Round and renormalize if necessary
  1.1102 × 2–3 (no change)
5. Determine sign: +ve × –ve  –ve
  –1.1102 × 2–3 = –0.21875

## Slide 68: Floating-Point Multiplication

## Slide 69: Integer-Multiplication Hardware
Initially 0

## Slide 70: Optimized Integer Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low

## Slide 71: FP Multiplier – Hardware Realization
integer multiplier

## Slide 72: FP Arithmetic: Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP  integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 73: FP Instructions in MIPS
FP hardware is Co-processor 1
  Adjunct processor that extends the ISA
Separate FP registers
  32 single-precision: $f0, $f1, … $f31
  Paired for double-precision: $f0/$f1, $f2/$f3, …
    Release 2 of MIPs ISA supports 32 × 64-bit FP reg’s
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  lwc1, swc1,
    e.g., lwc1 $f8, 32($sp)

## Slide 74: FP Instructions in MIPS
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
    e.g., add.s $f0, $f1, $f6
Double-precision arithmetic
  add.d, sub.d, mul.d, div.d
    e.g., mul.d $f4, $f4, $f6
Single- and double-precision comparison
Branch on FP condition code true or false

## Slide 75: FP Example: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in $f12, result in $f0, literals in global memory space
Compiled MIPS code:
f2c: lwc1 $f16, const5($gp) lwc2 $f18, const9($gp) div.s $f16, $f16, $f18 lwc1 $f18, const32($gp) sub.s $f18, $f12, $f18 mul.s $f0, $f16, $f18 jr $ra

## Slide 76: Summary
Computer arithmetic is constrained by limited precision
Bit patterns have no inherent meaning but standards do exist
  two’s complement
  IEEE 754 floating point
Computer instructions determine “meaning” of the bit patterns
Performance and accuracy are important so there are many complexities and implementation challenges in real machines

## Slide 77: Announcement of Next Test
Saturday, 17 October 2020
Time: 3:30 pm – 4:45 pm
Coverage: Computer Arithmetic
(Material taught in class during Sept. 28 – Oct. 08, 2020)
Question type: Short-Answer, MCQ