## Slide 1: CS 31007 Autumn 2020 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty
Bhargab B. Bhattacharya
Week 5, September 28, 2020
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 2: So far covered …
Evolution and history of computer design
Basic components of a computer
Instruction Set Architecture (ISA)
CPU Performance
MIPS Instruction Set, Programming
Acknowledgement: Patterson and Hennessy
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 3: The Instruction Set: a Critical Interface
instruction set
software
hardware
Quick Review

## Slide 4: Computer Design Approach
Instruction Set Architecture (ISA)
System software
(OS, Compiliers)
Computer Organization
Bottom-up approach:
Hardware first, ISA later
Instruction Set Architecture (ISA)
System software
(OS, Compiliers)
Computer Organization
Top-down approach to hardware design:
ISA first, hardware later

## Slide 5: What determines the execution time of a machine/assembly-level program P when it is run on a machine M?
P consists of a number of machine-level instructions (IC: instruction count);
Each machine instruction requires several clock cycles to complete (CPI: average number of clock cycles per instruction);
Each clock cycle has certain time period (CCT: clock cycle time)
Thus, CPU-time = IC  CPI  CCT
(CPU Performance Equation)

## Slide 6: Amdahl’s Law
CPU-timenew = CPU-timeold × (1 - Fracenhanced) + Fracenhanced
Speed-upoverall =
CPU-timeold
CPU-timenew
Speed-upenhanced
=
1
(1 - Fracenhanced) + Fracenhanced
Speed-upenhanced
Law of diminishing return: unaffected fraction will determine the limiting case!
Improvement of larger fraction will yield higher overall speed-up  Make the common case faster

## Slide 7: Execution Cycle
Instruction
Fetch
Obtain instruction from memory
Instruction
Decode
Determine required actions and instruction size
Operand
Fetch
Locate and obtain operand data from memory/register
Execute
Compute result value or status
Result
Store
Deposit results in register/memory for later use
Next
Instruction
Determine successor instruction
computer arithmetic, ALU design
operand-address computation

## Slide 8: Chapter 3
Arithmetic for Computers
Today’s Agenda

## Slide 9: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
  Hardware implementation of ALU
Floating-point real numbers
  Representation and operations
  Overflow and underflow
  Hardware implementation of FP-operations
§3.1 Introduction

## Slide 10: MIPS Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1
Make common operations faster …
Amdahl

## Slide 11
Bits carry no inherent meaning —steps in execution cycle define relationship between bits and their meaning
Binary numbers (base 2)
0000 0001 0010 0011 0100 0101 0110 0111 1000
Things to remember: number of bits is finite (finite-precision arithmetic)
what about overflow? fractions and real numbers negative numbers
How do we represent negative integers, real numbers?
Arithmetic needs a number system

## Slide 12
Sign Magnitude One's Complement Two's Complement
000 = +0 000 = +0 000 = +0 001 = +1 001 = +1 001 = +1 010 = +2 010 = +2 010 = +2 011 = +3 011 = +3 011 = +3
100 = -0 100 = -3 100 = -4 101 = -1 101 = -2 101 = -3 110 = -2 110 = -1 110 = -2 111 = -3 111 = -0 111 = -1
Issues: balance, number of zeros, ease of operations
Which one is suitable for computer arithmetic?
Possible Representations

## Slide 13: Number Dial: Signed-Magnitude Representation
A 4-bit signed-magnitude number representation system for integers
What is the range of representable numbers when n-bits are available?
-

## Slide 14: 2’s-Complement Number Dial
4-bit 2’s-complement number representation system for integers

## Slide 15: 2’s-Complement Number Systems
Evaluation of 2’s complement representation as decimal number

## Slide 16
32 bit signed numbers (2’s complement) 0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = + 1ten
0000 0000 0000 0000 0000 0000 0000 0010two = + 2ten ... 0111 1111 1111 1111 1111 1111 1111 1110two = + 2,147,483,646ten
0111 1111 1111 1111 1111 1111 1111 1111two = + 2,147,483,647ten
1000 0000 0000 0000 0000 0000 0000 0000two = – 2,147,483,648ten
1000 0000 0000 0000 0000 0000 0000 0001two = – 2,147,483,647ten
1111 1111 1111 1111 1111 1111 1111 1111two = – 1ten
maxint
minint
MIPS
What is the range of representable 2’s complement numbers when n-bits are available?

## Slide 17
Negating a two's complement number: invert all bits and add 1
  remember: “negate” and “invert” are quite different!
Converting an n-bit number into an equivalent number with more than n-bits (sign-extension):
  MIPS 16-bit “immediate” gets converted to 32-bits for arithmetic
  copy the most significant bit (the sign bit) and replicate it towards MSB
  0010 (+2) -> 0000 0010 (+2) 1010 (-6) -> 1111 1010 (-6)
Two's Complement Operations

## Slide 18: Example: MIPS Instruction Hardware needs to perform sign-extension before executing addition
An example of MIPS M/L instruction:
Total length of the instruction – 32 bits; opcode: 6 bits;
$t0, $s1 -> 32-bit CPU registers (ID: 5-bit each, as there are a total of 32 such registers); immediate value is provided as a 16-bit 2’s complement integer;
Add 5 to the content of $s1 and save the result in $t0
op
s1
t0
Immediate
6 bits
5 bits
5 bits
16 bits
addi $t0, $s1, 5
001000
10001
01000
0000000000000101

## Slide 19
Just like in grade school (carry/borrow 1s) 0111 0111 0110 + 0110 - 0110 - 0101
Two's complement operations easy
  subtraction using addition of negative numbers 0111 + 1010
Overflow (result too large for finite computer word):
  e.g., result of an arithmetic operation on two n-bit numbers exceeds the range of representable numbers Note that overflow term is somewhat misleading, it does not mean a carry has “overflowed”
Addition & Subtraction

## Slide 20: Signed-Magnitude vs 2’s-Complement
Signed-magnitude adder/subtractor is significantly complex
2’s-complement adder/subtractor needs very little hardware other than a simple adder

## Slide 21
Dilemma of Carry and Overflow
0 1 0 0
1 0 1 1
+
(+4)
(-5)
1 1 1 1
(-1)
no carry;
no overflow;
result correct
(-4)
1 1 0 0
0 1 1 0
+
(+6)
1 0 0 1 0
(+2)
carry discarded;
result still correct;
no overflow
1 0 0 0
1 0 0 0
+
(-8)
(-8)
1 0 0 0 0
(0)
carry ;
overflow ;
result invalid
0 1 0 0
0 1 0 0
+
(+4)
(+4)
1 0 0 0
(-8)
no carry;
overflow ;
result invalid
universe:
4-bit 2’s complement arithmetic
Decimal
0
0000
1
0001
2
0010
3
0011
4
0100
5
0101
6
0110
7
0111
2’s Complement
2’s Complement
1111
1110
1101
Decimal
-1
-2
-3
1100
1011
1010
1001
-4
-5
-6
-7
1000
-8

## Slide 22
No overflow when adding a positive and a negative number
No overflow when signs are the same for subtraction
Overflow occurs when the value affects the sign:
  overflow when adding two positives yields a negative
  or, adding two negatives gives a positive
  or, subtract a negative from a positive and get a negative
  or, subtract a positive from a negative and get a positive
Consider the operations A + B, and A – B
  Can overflow occur if B is 0 ?
  Can overflow occur if A is 0 ?
Hazards of Finite-Precision Arithmetic:
Detecting Overflow for Integer Operations

## Slide 23
Compute: X = A + B – C; A, B, C are +ve integers;
X = (A + B) – C
Or,
X = A + (B – C) ?
Hazards of Finite-Precision Arithmetic
The first choice might cause overflow – invalid result
The second option is safer

## Slide 24: CS 31007 Autumn 2020 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty
Bhargab B. Bhattacharya
Week 5, September 29, 2020
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 25
Computer Arithmetic
?

## Slide 26
Overflow Detection Logic: Hardware Solution
B: bn-1, bn-2, ……, b1, b0
S: sn-1, sn-2, ……, s1, s0
A: an-1, an-2, ……, a1, a0
Overflow = an-1bn-1sn-1 + an-1bn-1 sn-1
+
  overflow  adding two positives yields a negative
  or, adding two negatives gives a positive
sign-bit
In MIPS, on detecting overflow, interrupt (exception) is invoked;
add, addi (overflow considered); addu, addiu (overflow ignored)

## Slide 27
Overflow Detection Logic: Another Solution
Carry into MSB ° Carry out of MSB
  For a N-bit ALU: Overflow = CarryIn[N - 1] XOR CarryOut[N - 1]
A0
B0
1-bit
ALU
Result0
CarryIn0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
Overflow
X
Y
X XOR Y
0
0
0
0
1
1
1
0
1
1
1
0
Show that these two solutions are logically equivalent

## Slide 28: Integer Addition
Example: 7 + 6
§3.2 Addition and Subtraction
Overflow if result out of range
  Adding +ve and –ve operands, no overflow
  Adding two +ve operands
    Overflow if result sign is 1
  Adding two –ve operands
    Overflow if result sign is 0

## Slide 29: Integer Subtraction
Add negation of second operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range

## Slide 30: Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions
  On overflow, invoke exception handler
    Save PC in exception program counter (EPC) register
    Jump to predefined handler address
    mfc0 (move from coprocessor reg) instruction can retrieve EPC value, to return after corrective action

## Slide 31: Hardware for Arithmetic
Where we've been:
  Performance (seconds, cycles, instructions)
  Abstractions: Instruction Set Architecture Assembly Language and Machine Language
What's up ahead:
  Implementing the Architecture
32
32
32
operation
result
a
b
ALU

## Slide 32: Why Adders?
Addition: a fundamental operation
  Basic block of most arithmetic operations
  Address calculation
Faster, faster and faster
How?
  Architectural-level optimization
  Gate-level optimization
  Speed/area trade-off

## Slide 33: Review: 1-bit adder
One-bit Half Adder:
One-bit Full Adder:
Sum = A  B  Cin
Cout = A.B + B.Cin + A.Cin
FA
A
B
Cin
Cout
Sum
Sum = A  B
Cout = A.B
HA
A
B
Cout
Sum
A B Sum Cout
0 0 0 0
0 1 1 0
1 0 1 0
1 1 0 1
Cin A B Sum Cout
0 0 0 0 0
0 0 1 1 0
0 1 0 1 0
0 1 1 0 1
1 0 0 1 0
1 0 1 0 1
1 1 0 0 1
1 1 1 1 1
Notes: Can we use HA to add two n-bit numbers? No! Carry propagation.

## Slide 34: One-Bit Full-Adder (FA) Implementation
Sum = A  B  Cin
A
B
Cin
Sum
Cout = A.B + B.Cin + A. Cin
= A.B + Cin. (A+B)
A
B
A
B
Cin
Cout
FA
A
B
Cin
Cout
Sum
HMK: Implement FA using only nine 2-input NAND-gates;
only uncomplemented inputs (A, B, Cin) are available.

## Slide 35: n-bit Ripple-Carry Adder (RCA)
To add two n-bit numbers
C0
FA
a0
s0
b0
FA
a1
s1
b1
FA
a2
s2
b2
FA
an-1
sn-1
bn-1
Cn
. . .
N-bit RCA delay = n * 
 = (delay of 1-bit FA)
FA
A
B
Cin
Cout
Sum
Critical path in an n-bit ripple-carry adder
 CCT needs to accommodate long delay
Cost = O(n); delay O(n)
Flat Combinational Logic
Inputs: an-1, an-2, ……, a1, a0 ,bn-1, bn-2, ……, b1, b0
Outputs: sn-1, sn-2, ……, s1, s0, cn
B: bn-1, bn-2, ……, b1, b0
A: an-1, an-2, ……, a1, a0
Notes: What is C0? C_n?
This architecture is called Ripple-carry adder: the simplest!
Carry delay is important

## Slide 36: 4-bit Ripple-Carry Addition: Example
C0
FA
A0
S0
B0
FA
A1
S1
B1
FA
A2
S2
B2
FA
A3
S3
B3
C4
C1
C2
C3
T=1
0
0
1
0
1
0
0
1
0
0
1
0
0
1
1
1
0
0
0
0
0
0
0
0
0
T=0
B=0101
A=0011
S=0000
S=0110
0
0
1
0
0
1
0
1
T=2
S=0100
0
0
0
1
0
1
0
1
T=3
S=0000
1
0
0
1
0
1
0
1
T=4
S=1000
delay = 4 units; also, overflow has occurred
Notes: The time unit is the delay for one full adder to compute its S and Cout signals
What is the meaning of the intermediate (T=1..3) values of S?
How long should the clock period be?
What effect does the carry chain delay have on the clock frequency?

## Slide 37: Subtraction using 2’s complement

## Slide 38: Multi-Bit Adders

## Slide 39: Ripple-Carry Adder
Chain 1-bit adders together
Carry ripples through the entire chain
Disadvantage: slow

## Slide 40
Possible solutions to mitigate
carry-propagation delay
1. Detect the end of carry propagation rather than wait for
the worst-case time
2. Speed-up propagation using techniques such as
  lookahead
  carry-select
  logarithmic adder
3. Limit carry propagation to within a small number of bits
4. Trade-off: speed (or inversely, delay) versus logic cost

## Slide 41: Adder
Several types of carry-propagate adders (CPAs) are:
  Ripple-carry adders (slow)
  Carry-lookahead adders (fast)
  Prefix adders (faster)
Carry-lookahead and prefix adders are faster for large adders but require more hardware
  Symbol

## Slide 42
Carry Lookahead Adder (CLA): Basic Idea
B: bn-1, bn-2, .., bi ,…,b1, b0
S: sn-1, sn-2, ……, s1, s0
A: an-1, an-2, .., ai…, a1, a0
At the ith stage, carry will be generated for propagation to the next stage if and only if
ai = bi = 1; => gi = ai bi ==> carry-generate function
or either ai or bi = 1, and previous carry ci -1 arrives here;
=> pi = ai + bi => carry-propagate function
+
ith-bit
carry-bit ci

## Slide 43: Carry-Lookahead Adder
Generate all carry bits directly from inputs, instead of rippling through FA-blocks sequentially
Few notation:
  Generate (gi) and propagate (pi) signals for each bit:
    A column will generate a carry out if ai AND bi are both 1.
  gi = ai bi
    A column will propagate a carry in to the carry out if Ai OR Bi is 1.
  pi = ai + bi
    The carry out of a column (Ci) is:
  ci+1 = ai bi + (ai + bi )ci = gi + pi ci

## Slide 44: Carry-Lookahead Adder
    The carry out of a column (Ci) is:
  ci+1 = ai bi + (ai + bi )ci = gi + pi ci
We can visualize the carry “generate” and “propagate” functions from another perspective:
Ci+1 = a.b + b. cin + a. cin
= a.b + cin. (a+b)
    A column will generate a carry out if ai AND bi are both 1, i,e., gi = ai bi
    A column will propagate a carry if Ai or Bi is 1, i.e.,
    pi = ai + bi

## Slide 45: Carry-Lookahead Adder
Idea:
  Produce ci ahead of time instead of passing through (i-1) stages
Bit position
Carry
A
B
Sum
7 6 5 4 3 2 1 0
1 0 0 1 1 1 1
0 1 0 0 1 1 0 1 +
0 1 0 0 0 1 1 1
1 0 0 1 0 1 0 0
FA
FA
FA
FA
FA
Instead of RCA, use independent 1-bit FA-modules
no signal propagation through stages
Notes: In the example,
By looking at (A4,B4), we can say for sure that C5=0, no matter what C4 is.
By looking at (A2,B2), we can say for sure that C3=1.
C3, “generated” by (A2,B2) (or by A0,B0 if you wish), “propagated” as far as C4, and then got “killed” by (A4,B4)
The idea is, can we look at A(3..0) and B(3..0) and determine the value of C4 in one shot?

## Slide 46: Carry-Lookahead Adder
Instead of RCA, use n independent 1-bit FA-modules working in parallel;
no signal propagation through stages; directly generate all
carry-bits from inputs
C0
FA
A0
S0
B0
FA
A1
S1
B1
FA
A2
S2
B2
FA
A3
S3
B3
C4
C1
C2
C3
RCA
C0
FA
A0
S0
B0
FA
A1
S1
B1
FA
A2
S2
B2
FA
A3
S3
B3
C4
C1
C2
C3
CLA
Notes: In the example,
By looking at (A4,B4), we can say for sure that C5=0, no matter what C4 is.
By looking at (A2,B2), we can say for sure that C3=1.
C3, “generated” by (A2,B2) (or by A0,B0 if you wish), “propagated” as far as C4, and then got “killed” by (A4,B4)
The idea is, can we look at A(3..0) and B(3..0) and determine the value of C4 in one shot?

## Slide 47
Basic Signals
Generate signal: gi = aibi
Propagate signal: pi = ai + bi
ci+1 = gi + cipi
Carry recurrence

## Slide 48
Unrolling Carry Recurrence
ci = gi-1 + ci-1pi-1 =
= gi-1 + (gi-2 + ci-2pi-2)pi-1 = gi-1 + gi-2 pi-1 + ci-2pi-2pi-1 =
= gi-1 + gi-2 pi-1 + (gi-3 + ci-3pi-3)pi-2pi-1 =
= gi-1 + gi-2 pi-1 + gi-3 pi-2pi-1 + ci-3pi-3pi-2pi-1 =
= ….. =
= gi-1 + gi-2 pi-1 + gi-3 pi-2pi-1 + gi-4pi-3pi-2pi-1 + ….. +
+ g0p1p2…pi-2pi-1 + c0p0p1p2…pi-2pi-1 =
= gi-1 +  gk  pj + c0  pj
k=0
i-2
j=k+1
i-1
j=0
i-1

## Slide 49
4-bit Carry-Lookahead Adder
c4 = g3 + g2 p3 + g1 p2p3 + g0p1p2p3 + c0p0p1p2p3
c3 = g2 + g1 p2 + g0 p1p2 + c0p0p1p2
c2 = g1 + g0 p1 + c0p0p1
c1 = g0 + c0 p0
s0 = x0  y0  c0 = p0  c0
s1 = p1  c1
s2 = p2  c2
s3 = p3  c3
gi = aibi
pi = ai + bi

## Slide 50: Carry Lookahead Adder
C1 = a0b0 + (a0+b0)c0 = g0 + p0c0
C2 = a1b1 + (a1+b1)c1 = g1 + p1c1 = g1 + p1g0 + p1p0c0
C3 = a2b2 + (a2+b2)c2 = g2 + p2c2 = g2 + p2g1 + p2p1g0 + p2p1p0c0
C4 = a3b3 + (a3+b3)c3 = g3 + p3c3 = g3 + p3g2 + p3p2g1 + p3p2p1g0 + p3p2p1p0c0
gi = aibi pi = ai + bi
a3 b3
g3
p3
a2 b2
g2
p2
a1 b1
g1
p1
a0 b0
g0
p0
c1
c2
c3
c4
c0
carry-bits
CLA logic
inputs
one AND-gate and
one OR-gate

## Slide 51: Carry Generation Logic

## Slide 52
4-bit CLA Logic
gi = aibi
pi = ai + bi
B: b3 b2 b1 b0
A: a3 a2 a1 a0
all carry-bits are generated directly from inputs;
one can thus use independent FA-modules, to produce the sum-bits in parallel!

## Slide 53
n-bit CLA Adder
Much faster than RCA
Critical path delay in an n-bit CLA?
Cost = O(?); delay O(?)

## Slide 54: Full Carry Lookahead
Theoretically, it is possible to derive each sum digit directly from the inputs that affect it
Carry-lookahead adder is impractical for large n
s0
s1
s2
s3
b0
b1
b2
b3
a0
a1
a2
a3
cin
. . .

## Slide 55
n-bit Hybrid CLA Adder
Implementation of lookahead for the complete adder is impractical because of cost
    Divide n stages into smaller groups
    Full carry lookahead within each group
    Ripple carry among groups

## Slide 56: 12-Bit Hybrid (CLA + RCA)
p,g
p,g
p,g
p,g
S0
S1
S2
S3
S4
S5
S6
S7
p,g
p,g
p,g
p,g
B0
B1
B2
B3
B5
B6
B7
B4
C0
C4
Carry Generator
Carry Generator
C8
S8
S9
S10
S11
p,g
p,g
p,g
p,g
B9
B10
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
B11
B8
Carry Generator
C12
0111
1101
0110
1001
1101
1010
0
B=
A=
Trade-off: cost versus delay
Another solution: 12-Bit Hybrid (RCA + CLA)??
Cost = O(?); delay O(?)
CLA
RCA
Notes: The timing is not realistic. I have assumed:
  p_i and g_i computations take 1 cycle
  Carry generation block take 1 cycle to generate the last carry
  Hence, the second row shows T=2 (p,g calc + carry gen), while other rows show 1 cycle (only carry generation)

## Slide 57: 32-bit Hybrid CLA with 4-bit blocks (CLA + RCA)

## Slide 58: CLA principle can be used recursively to build bigger adders => Carry-lookahead tree (CLT)
A 16 bit adder uses four 4-bit adders
It takes block g and p terms and cin to generate block carry bits out
Block carries are used to generate bit carries
  could use ripple carry of 4-bit CLA adders
  Better: use the CLA principle again!

## Slide 59
g15p15
16-bit 2-level Carry-Lookahead Adder (CLT)
CLA GEN
c1
c2
c3
g[0,3]
p[0,3]
g0p0
g1p1
g2p2
g3p3
c0
CLA GEN
c5
c6
c7
g[4,7]
p[4,7]
g4p4
g5p5
g6p6
g7p7
c4
CLA GEN
c9
c10
c11
g[8,11]
p[8,11]
g8p8
g9p9
g10p10
g11p11
c8
CLA GEN
c13
c14
c15
g[12,15]
P[12,15]
g12p12
g13p13
g14p14
c12
CLA GEN
g[0,15]
p[0,15]
(carry-lookahead tree - CLT)
Cost = O(?); delay O(?)

## Slide 60
64-bit 3-level Carry-Lookahead Adder (CLT)
g[16,19]
p[16,19]
c16
g[20,23]
p[20,23]
c20
g[24,27]
p[24,27]
c24
g[28,31]
p[28,31]
c28
CLA GEN
g[16,31]
p[16,31]
CLA GEN
CLA GEN
CLA GEN
CLA GEN
CLA GEN
c0
c31 c30 c29
c27 c26 c25
c23 c22 c21
c19 c18 c17
g[0,15]
p[0,15]
g[32,47]
p[32,47]
g[48,63]
p[48,63]
c32
c48
g[0,63]
p[0,63]

## Slide 61
Carry-Select Adders (CSA)
Idea:
Compute sum-bits in parallel for two possible carry-bits;
When the previous carry really arrives, just select the pre-computed “sum”.
CLA: Looking ahead in time (pre-compute carry-bits)
CSA: Looking ahead in space (pre-compute sum-bits)

## Slide 62
k-bit Carry-Select Adder
sum-bits
carry-out
Units: cost and delay of a single 2-to-1 multiplexer

## Slide 63
Multi-level k-bit Carry-Select Adder

## Slide 64
Pitfalls of CLA Adder
Implementation of lookahead for the complete adder is impractical because of cost
Analyze the implementation complexity of CLA

## Slide 65: CS 31007 Autumn 2020 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty
Bhargab B. Bhattacharya
Week 5, October 01, 2020
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 66: So far covered in computer arithmetic…
Number Systems and Overflow
Ripple-Carry Adder (RCA)
Carry-Lookahead Adder (CLA)
Hybrid Adder, CLT
Carry-Select Adder (CSA)
Brent-Kung’s Parallel Prefix Adder (PPA)
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 67: Carry Lookahead Adder
C1 = a0b0 + (a0+b0)c0 = g0 + p0c0
C2 = a1b1 + (a1+b1)c1 = g1 + p1c1 = g1 + p1g0 + p1p0c0
C3 = a2b2 + (a2+b2)c2 = g2 + p2c2 = g2 + p2g1 + p2p1g0 + p2p1p0c0
C4 = a3b3 + (a3+b3)c3 = g3 + p3c3 = g3 + p3g2 + p3p2g1 + p3p2p1g0 + p3p2p1p0c0
gi = aibi pi = ai + bi
a3 b3
g3
p3
a2 b2
g2
p2
a1 b1
g1
p1
a0 b0
g0
p0
c1
c2
c3
c4
c0
carry-bits
CLA logic
inputs
one AND-gate and
one OR-gate

## Slide 68
4-bit Carry-Lookahead Adder
c4 = g3 + g2 p3 + g1 p2p3 + g0 p1p2p3 + c0 p0p1p2p3
c3 = g2 + g1 p2 + g0 p1p2 + c0 p0p1p2
c2 = g1 + g0 p1 + c0 p0p1
c1 = g0 + c0 p0
gi = aibi
pi = ai + bi
cn => last term would be p0p1p2……..pn-1
In general, the problem boils down to =>
How to compute efficiently in reasonable cost and time:
x0 , x0x1, x0 x1x2, x0x1x2 x3, …., x0x1 x2x3 …xn-1
(Prefix-sum/product problem)
inputs

## Slide 69: Brent-Kung’s Prefix Tree: Logarithmic-Delay
x
0
x
1
x
2
x
3
x
4
x
5
x
6
x
7
x
8
x
9
x
10
x
11
x
12
x
13
x
14
x
15
s
0
s
1
s
2
s
3
s
4
s
5
s
6
s
7
s
8
s
9
s
10
s
11
s
12
s
13
s
14
s
15
1
2
3
4
5
6
Level
AND-gate
fanout
x0x1x2 x3 x0 x1x2 x0x1 x0
delay = O(log n);
cost = O(nlog n);
fanout O(n);
cost = O(n2log n)?
Notes: - One disadvantage of this adder is the high fanout of the output of C7. Other adder structures like the Kogg-Stone tree are designed to reduce the fanout.

## Slide 70: Brent-Kung Parallel-Prefix Adder (log-delay)
ci+1 = gi + cipi
delay = O(log n);
cost = O(nlog n);
fanout O(n);
cost = O(n2log n)?

## Slide 71: Carry-Save Addition: Adding multiple operands
Consider adding six set of numbers (4 bits each in the example)
The numbers are 1001, 0110, 1111, 0111, 1010, 0110 (all unsigned +ve)
One way is to add them pair wise, getting three results, and then adding them again
1001 1111 1010 01111 100101
0110 0111 0110 10110 10000
01111 10110 10000 100101 110101
Other method is add them three at a time by saving carry
1001 0111 00000 010101 001101
0110 1010 11110 010100 101000
1111 0110 01011 001100 110101
00000 01011 010101 001101 SUM
11110 01100 010100 101000 CARRY
final sum

## Slide 72: CARRY-SAVE ADDER (addition of multiple operands)
Add four 4-bit integers, A, B, E, F
Cost = O(?); delay O(?)

## Slide 73: Adding m n-bit numbers with CSA and log-adder
Wallace tree;
Delay = O(logm + lg (n + logm))
Linear chain;
Delay = O(m + lg (n + m))
depth = log3/2m
LCA: Lookahead carry adder with log-delay (~CLT)